TRSE Stage Specifications

Width of Prosc		6920mm

Height of  Prosc		6450mm

Full depth of stage		11570mm

Dock doors			2100mm wide 5000mm High

Raked Stage 		            1:20

Depth to second prosc		5140mm

Height to grid			1190mm Upstage

1245mm Downstage

Height of second prosc	6220mm

Height under clearing floor	6180mm

Height under DS fly floor	6150mm

Height under US fly floor	6360mm

Number of Bars		37 (33 hemp (120kg max UDL), 3 motors (2@300kg, 1@220kg), 1 winch)

6 x 500kg chain blocks

Trap space 			DS edge 2085 US of rear Iron Line

(not permanent)		US edge 3375 US of rear Iron Line

Width 800

Depth 1290

On centre

Distance between fly floors	9478mm

Distance US fly floor to wall	8305mm

Bar Length / SWL	            House border bar winch 7700mm 300kgs

House tab bar motor 7810mm 250kgs

Downstage Hemps 1-15 9000mm  120kgs ( 200kgs with Chain Blocks )

Upstage Hemps 16-33 8000mm ( 200kgs with Chain Blocks )

Dock Length			9250   Dock width			4000

4 counterweight assists, 200kgs max per cradle, 650kg in Bricks available ( cradle weight 25kg )

Rigging time = 4 hours per Assist, with 3 people

Stage Inventory TRSE

Soft Legs

Serge		2.4 x 6.5m	x 6

1.2 x 6m	x2

Soft Borders

Serge		9 x 2.4m	x6

Serge		9 x 3.6m          x1

Full Blacks

Serge 		8 x 6.5m        x 2

Serge	            8 x 6m           x 2

Serge               6 x 6m           x1

Hard Masking Flats

Serge		2 x 6m				x4

Serge		1 x 6m				x4

Serge		1 x 6.5m			x4

Serge               0.5 x 6m                                  x2

Serge		assortment of various odd smaller sizes

Screens

BP		9.2m x 5.5m grey (somewhat dirty)

BP		6.5m x 6.5m (couple of paint marks)

Cyclorama	12m x 9m

White Cyc	8m x 6.5m  x2

Black Gauze	9m x 9m

White Gauze   ?

House Tabs

Tabs		4.2m x 5.5m			x2  
Tab Border	7.2 x 1.2m

Steel Decks

8ft by 4ft        x 15  ,   4ft by 4ft   x  1 ,  2m by 1m   x  2